| Mobile Plant Type | Amber beacon | Brake lights & turn signals | Headlights, tail lights , Working Lights & or clearance lights | Rear reflectors | Rear & side reflective tape | Rear & Side vision mirror(s) | Horn | Reverse alarm | Reverse Camera | Brakes | Park Brake | UHF Radio | Seat Belt | Skyguard operator protection system or equivalent fitted | Operator Protective Structure - Rollover (ROPS/TOPS) | FOPS/Operator protective guarding | Lifting / Anchor point | Fire Extinguisher | Steering Systems | Decals and Safety Signage | Neutral Start | Battery Isolator- key lockable | Access: Guardrail system on Machine Decks/ Platforms/ steps & Grab rails | Anti-drop/Burst Protection (or control lowering device) on load hydraulics/boom | Emergency Stop | Compliant Quickhitch with positive lock | Registration / Label / Plates | Machinery Guarding | Daily Inspection Form | Design / Item Registration | Provision of information including OEM Manual, SWMS, Plant Risk Assessment |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Backhoe Loader | M | M | M | M | M | M | M | M | AR | M | M | M | M |  | M | M | AR | M | M | M | M | M | M | AR | M | M | M | AR | M |  | M |  |
| Compactor (soil or landfill) | M | M | AR | M | M | M | M | M | M | M | M | M | M |  | M | M |  | M | M | M | M | M | M |  | M |  | M | AR | M |  | M |  |
| Concrete Pump/Placing Units - Truck Mounted | M | M | AR | M | M | M | M | M | M | M | M | M | M |  |  |  |  | M | M | M | M | M | M | M | M |  | M | AR | M | M | M |  |
| Concrete Agitator Truck (Road-registered) | M | M | M | M | M | M | M | M | M | M | M | M | M |  |  |  |  | M | M | M | M | M | M |  | AR |  | M | AR | M |  | M |  |
| Crane - Crawler | M | AR | AR | M | M | M | M | M | M | M | M | M | M |  | AR | AR | M | M | M | M | M | M | M | M | M |  | AR | AR | M | M (>10t) | M |  |
| Crane - Mobile | M | M | M | M | M | M | M | M | M | M | M | M | M |  | AR | AR | M | M | M | M | M | M | M | M | M |  | M | AR | M | M (>10t) | M |  |
| Crane - Gantry | M |  | AR | M | M |  | AR | AR | AR | M | M | M | AR |  |  |  | M | M | M | M | M | M | M | M | AR |  | AR | AR | M | M (>5t) | M |  |
| Crane - Tower |  |  | AR | M | M |  | AR | AR | AR | M | M | M | AR |  |  |  | M | M | M | M | M | M | M | M | AR |  | AR | AR | M | M | M |  |
| Crane – Vehicle Loading / Hiab | M | M | M | M | M | M | M | M | M | M | M | M | M |  | AR |  | M | M | M | M | M | M | AR | M | M |  | M | AR | M | M | M |  |
| Crusher | M |  | M | AR | M |  | M | M | AR | M | M | AR | AR |  | AR | AR |  | M | M | M | M | M | M |  | M |  | AR | AR | M |  | M |  |
| Dozer | M |  | AR | M | M | M | M | M | M | M | M | M | M |  | M | M |  | M | M | M | M | M | M |  | M |  | M | AR | M |  | M |  |
| Drilling Rig ] | M |  | AR | AR | M | M | M | M | AR | M | M | AR | AR |  | AR | AR |  | M | M | M | M | M | AR | AR | M | AR | AR | AR | M |  | M |  |
| Dump Truck - Off-road (Articulated and Rigid) | M | M | M | M | M | M | M | M | M | M | M | M | M |  | M | M |  | M | M | M | M | M | M |  | M |  | M | AR | M |  | M |  |
| Elevated Work Platform (EWP) - Truck mounted Boom | M | M | M | M | M | M | M | M | AR | M | M | M | M |  |  | TBD | M | M | M | M | M | M | M | M | M |  | M | AR | M | M (>2.4m) | M |  |
| EWP - Self-propelled Boom-type Lift | M | AR | AR | M | M |  | AR | M | AR | M | M | AR |  | M |  | TBD | M | M | M | M | M | M | M | M | M |  | AR | AR | M | M (>2.4m) | M |  |
| EWP - Self-propelled Scissor Lift | M | AR | AR | M | M |  | AR | M | AR | M | M | AR |  | M |  | TBD | AR | M | M | M | M | M | M | M | M |  | AR | AR | M |  | M |  |
| Excavator - Compact (i.e. less than 6t) | M |  | M | M | M | M | M | M | AR | M | M | AR | M |  | M | M | AR | M | M | M | M | M | AR | AR | M | M | M | AR | M |  | M |  |
| Excavator: 6t to 50t (includes excavator-like machines) | M |  | M | M | M | M | M | M | M | M | M | M | M |  | M | M | AR | M | M | M | M | M | M | AR | M | M | M | AR | M |  | M |  |
| Forklift / Industrial Lift truck | M | AR | AR | M | M | M | M | M | AR | M | M | AR | M |  | AR | M | AR | M | M | M | M | M | M | M | M |  | M | AR | M |  | M |  |
| Grader | M | M | M | M | M | M | M | M | M | M | M | M | M |  | M | M |  | M | M | M | M | M | M |  | M |  | M | AR | M |  | M |  |
| Loader | M | M | M | M | M | M | M | M | M | M | M | M | M |  | M | M | AR | M | M | M | M | M | M | AR | M | AR | M | AR | M |  | M |  |
| Roller - 3 Point | M | M | M | M | M | M | M | M | AR | M | M | M | M |  | M | M |  | M | M | M | M | M | M |  | M |  | M | AR | M |  | M |  |
| Roller - Multi tyred | M | M | M | M | M | M | M | M | AR | M | M | M | M |  | M | M |  | M | M | M | M | M | M |  | M |  | M | AR | M |  | M |  |
| Roller - Pad Foot | M | M | M | M | M | M | M | M | AR | M | M | M | M |  | M | M |  | M | M | M | M | M | M |  | M |  | M | AR | M |  | M |  |

| Mobile Plant Type | Amber beacon | Brake lights & turn signals | Headlights, tail lights , Working Lights & or clearance lights | Rear reflectors | Rear & side reflective tape | Rear & Side vision mirror(s) | Horn | Reverse alarm | Reverse Camera | Brakes | Park Brake | UHF Radio | Seat Belt | Skyguard operator protection system or equivalent fitted | Operator Protective Structure - Rollover (ROPS/TOPS) | FOPS/Operator protective guarding | Lifting / Anchor point | Fire Extinguisher | Steering Systems | Decals and Safety Signage | Neutral Start | Battery Isolator- key lockable | Access: Guardrail system on Machine Decks/ Platforms / steps and grab rails | Anti-drop/Burst Protection (or control lowering device) on load hydraulics/boom | Emergency Stop | Compliant Quick hitch with positive lock | Registration / Label / Plates | Machinery Guarding | Daily Inspection Form | Design Registration | Provision of information including OEM Manual, SWMS and Plant Risk Assessment |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Roller - Drum | M | M | M | M | M | M | M | M | AR | M | M | M | M |  | M | M |  | M | M | M | M | M | M |  | M |  | M | AR | M |  | M |
| Roller - Tandem drum | M | M | M | M | M | M | M | M | AR | M | M | AR | M |  | M | AR |  | M | M | M | M | M | M |  | M |  | M | AR | M |  | M |
| Paver | M | AR | AR | AR | M | M | M | M | AR | M | M | AR | AR |  | AR | AR |  | M | M | M | M | M | M |  | M |  | M | AR | M |  | M |
| Piling Rig | M |  | AR | AR | M | M | AR | M | AR | M | M | AR | AR |  | AR | AR |  | M | M | M | M | M | M | AR | M |  | AR | AR | M |  | M |
| Pipe Layers | M | AR | AR | AR | M | AR | AR | M | AR | M | M | AR | AR |  | AR | AR |  | M | M | M | M | M | AR | AR | AR |  | AR | AR | M |  | M |
| Profiler | M | M | M | M | M | M | M | M | AR | M | M | AR | AR |  | AR | AR |  | M | M | M | M | M | M | AR | AR |  | M | AR | M |  | M |
| Scraper | M | M | M | M | M | M | M | M | M | M | M | M | M |  | M | M |  | M | M | M | M | M | M |  | AR |  | M | AR | M |  | M |
| Screen | M |  | AR | AR | M | AR | AR | M | AR | M | M | AR | AR |  | AR | AR |  | M | M | M | M | M | M |  | AR |  | AR | AR | M |  | M |
| Skid Steer Loader | M | AR | M | M | M | M | M | M | M | M | M | M | M |  | M | AR | AR | M | M | M | M | M | M | AR | AR | AR | M | AR | M |  | M |
| Soil Stabiliser | M | M | AR | M | M | AR | AR | M | AR | M | M | AR | AR |  | AR | AR |  | M | M | M | M | M | AR |  | AR |  | AR | AR | M |  | M |
| Sweeper | M | M | M | M | M | M | M | M | AR | M | M | M | M |  | AR | AR |  | M | M | M | M | M | AR |  | AR |  | M | AR | M |  | M |
| Telescopic Material Handler | M | M | M | M | M | M | M | M | M | M | M | M | M |  | M | AR | M | M | M | M | M | M | M | M | M | AR | M | AR | M | M >10t | M |
| Tractor | M | AR | M | M | M | M | M | M | AR | M | M | M | M |  | M | AR |  | M | M | M | M | M | M | AR | M | AR | M | AR | M |  | M |
| Trenchers - Ride On | M | AR | AR | AR | M | AR | AR | M | AR | M | M | AR | AR |  | AR | AR |  | M | M | M | M | M | M | M | M |  | M | AR | M |  | M |
| Lime / Cement Spreaders | M | AR | AR | AR | M | AR | AR |  | AR | M | M | AR | AR |  | AR | AR |  | M | M | M | M | M | AR |  | AR |  | AR | AR | M |  | M |
| Legend: Mandatory at all times ( No Exemption ) Mandatory with Conditional Operation. 5 day repair period permitted. Risk Assessment and specific controls are required As required ( Project Determination ) and determined by Risk Assessment. |  |  |  | Note 1: For further information and detail relating to Mobile Plant inspection criteria see document – Gateway South: Mobile Plant – Safety Compliance Guide. Note 2: For Item / Design registration details see document - Guide for applicants for plant design registration, January 2012 Note3: Refer to local Road & or Transport Authorities for specific registration requirements for mobile plant Note 4 : Projects must review this matrix against any further local, site specific or client requirements and supplement this Matrix where required Note 5: For further information relating to ROPS/FOPS/TOPS and OPG refer to document – Gateway South; ROPS and FOPS guide Note 6: Any plant used to lift freely suspended loads must be compliant with document – Gateway South: Lifting Using Earthmoving Mobile Equipment Work Instruction |