# LOCATING SEQUENTIAL STRINGS – Vegetation and Trees

| CODE | PTRU |
| --- | --- |
| DESCRIPTION | Undersized Trunk - Tree >2m Tall |
| MODEL | XSURVEY |
| TINNABLE | NO |
| DIRECTIONAL |  |
| LOCATION INFORMATION | Locate at centre |
| COMMENTS | Trunk Diameter <150mm |

| CODE | PTRZ |
| --- | --- |
| DESCRIPTION | Significant Tree |
| MODEL | XSURVEY |
| TINNABLE | NO |
| DIRECTIONAL |  |
| LOCATION INFORMATION | Locate at centre |
| COMMENTS |  |

| CODE | PTR* |
| --- | --- |
| DESCRIPTION | Trunks between 150 mm and 625 mm diameter. |
| MODEL | XSURVEY |
| TINNABLE | NO |
| DIRECTIONAL |  |
| LOCATION INFORMATION | Locate at centre |
| COMMENTS | Spreads as listed below |
| Code Spread (Metres) Code Spread (Metres) PTRT < 1.5 PTRL 7-10 PTRS 1.5 - 3 PTRX >10 PTRM 3-7 |

| CODE | EV |
| --- | --- |
| DESCRIPTION | Edge of Vegetation |
| MODEL | SURVEY MODEL |
| TINNABLE | YES |
| DIRECTIONAL | YES |
| LOCATION INFORMATION |  |
| COMMENTS | Isolated dense cluster of vegetation |

| CODE | PSHH |
| --- | --- |
| DESCRIPTION | Shrub |
| MODEL | XSURVEY |
| TINNABLE | NO |
| DIRECTIONAL |  |
| LOCATION INFORMATION | Locate at centre |
| COMMENTS |  |

# Text boxes

Greater than 625mm

Tree Taller than 2m

Less than 150mm

Less than 1.5m

Spread